# Array Types
The library includes several lightweight array types.
### Array< Type >
Dynamic Array type. Similar in function to an STL vector.
### StaticArray< Type, MaxSize >
Static Array type. Syntax is the same as the dynamic array, except you must know how large this will ever get. This class can be used to support dynamic array function in static scope (i.e. To locally create a dynamic array on the stack).
### WrapArray< Type, MaxSize >
A variation of StaticArray. This one allows fast adding of entries on to the front, as well as the back of the array. The trade off is a slower indexing time. For a better version of this, see PowerWrapArray.
### PowerWrapArray< Type, MaxSize >
A much faster version of wrap array, that should only require 1 extra cycle per lookup. However, the tradeoff is MaxSize MUST be a power of 2. I.e. 2, 4, 8, 16, 32, 64, 128, 256, 512, 1024, 2048, 4096, 8192, 16384, and so on.

## Functions
Constructor can take a size as an argument.
Array can be indexed like a C style array. MyArray[10] = “FishSticks”;

Array.Size() returns the current size of the array.
Array.MaxSize() returns the maximum possible size (without resizing, where appropriate).

Array.Resize( Size ) to resize the array to a specific size.
Array.Reallocate( Size ) to change the maximum size of an Array (Array type only).

Array.PushBack( Value ) to add a new entry on to the back of the Array.
Array.PopBack( Value ) to remove an entry from the back, and return it.
Array.PushFront( Value ) to add a new entry on to the front of the Array. (WrapArray's only)
Array.PopFront( Value ) to remove an entry from the front, and return it. (WrapArray's only)
# Set Types

### ABC Sets
The ABSet, ABCSet, ABCDSet and ABCDESet types

### RGB Sets
Specialty RGBSet, and RGBASet too. BGRSet and BGRASet for nice order swapping unions.

### UV Set
UVSet, for UV co-ordinates.